HILOAD

              An utility for loading TSR's someplace else
                                   by
                             Larry Shannon
                              18 Jun 1989

HILOAD is a utility program designed to load your normal TSR 
(Terminate-and-Stay-Resident) programs somewhere else in memory. Usually 
this is a place outside the normal DOS region; that is, outside the 
first 640K of system memory.

At this time, it does not include either extended or expanded memory.


                               BACKGROUND

The 8088 used in the PC-XT is capable of addressing up to 1024K of 
memory.  The designers of the PC and DOS decided that only the first 
640K would be used by the operating system, DOS, and the rest was 
reserved for other uses.

Because of the way the 8088 forms addresses, it is customary to refer to 
addresses by a segment:offset combination. The 'actual' final address is 
formed by multiplying the segment value by 16 (i.e., shifting it left 4 
places) and adding the result to the offset address.

        Thus, the very first address in the machine is called 0000:0000.
An address 1024 bytes from this start (hex 400) may be variously
indentified as 0000:0400, 0040:0000, 0020:0200, 0038:0080, etc.

For convenience, we may speak of the various segments as:

        0000:0000       to      0000:FFFF       Block 0
        1000:0000       to      1000:FFFF       Block 1

                    and so on

        E000:0000       to      E000:FFFF       Block E
        F000:0000       to      F000:FFFF       Block F

It is easy to see that there are 16 contiguous segments of 64K each, 
yielding (16 X 64 =) 1024K, or one megabyte, and that DOS can only use 
the first 10 segments, or blocks 0 through 9.

What is in the other 6 segments?  Is that 384K of potential memory just 
sitting there idle?


                           WHO'S USING WHAT?

Well, actually not. Some of these blocks have been set aside, and are 
probably being used, for specific purposes.

Block F is where the ROM BIOS lives and, if you have a true- blue IBM 
PC, where the ROM BASIC lives.  So the F block is pretty well spoken 
for.

Block B is where the memory for the video sits.  If you have a 
Monochrome Display Adapter (MDA), it uses 4K of memory at addresses 
B000:0000 to B000:1000, and the remainder of the B block, 60K, is 
unused. In fact, if you have a straight monochrome card like IBM 
supplies, that's all the memory you have available.

If you have a Color Graphics Adapter (CGA), it occupies memory from 
B800:0000 to B800:7FFF (or equivalently B000:8000 to B000:FFFF). Like 
the MDA, when the CGA is in text mode it only uses the first 4K of this 
memory, but it can support up to 8 'pages' of 4K each; when in graphics 
mode, all 32K are in use. Like the MDA, true-blue CGA cards, and most 
clone CGA cards, have only that 32K available.

Enhanced Graphics Adapters (EGA) are even bigger consumers of memory, at 
maximum using the A block and part of the C block!

If you have a hard disk, its BIOS is normally located on the hard disk 
controller card, and is ususlly resident at C000:8000, or as it is 
commonly referred to, C800:0000.


                                SO WHAT?

Astute observers will notice that the D and E blocks were pretty much 
left out of the above description.  It is believed that these areas of 
memory were set aside by IBM for program cartridges, but few, if any, of 
these were actually produced, and this area is normally wide open and 
available for use.

If you are like most PC users, you have only a monochrome or CGA 
display, and the A block is available to you also.


                            DOWN TO BUSINESS

The '640K barrier' people talk about is caused by two reasons: programs 
are getting more sophisticated and user-friendly, meaning they take up 
more memory.  Secondly, there has been a proliferation of many handy 
programs that reside in memory (TSR's) which 'pop up' with useful 
information at the touch of a key or perform some other action.  
Examples are SideKick from Borland International, various printer 
buffers which are almost a necessity, and so on.  It is not too unusual 
to have half one's DOS memory taken up with various TSR's.

While there's little we can do about fat programs, we can move these 
TSR's out of the way. This was the driving force behind the development 
of HILOAD.

                      WHERE DO I GET THIS MEMORY?

Some PC clone makers map their memory into the D and E blocks; Kaypro 
for one does, others may also. Constructing a board to fill in these 
holes is not difficult, especially if static RAMS (SRAM) are used; these 
are now available in 32K X 8 sizes at attractive prices.

An old trick is to use commercial memory cards (now obsolete but 
available) that allow themselves to be mapped into the desired regions.

Finally, users of Hercules Graphics cards and their clones usually have 
the full 64K in the B block available, but only 4K is used in text mode.  
That 60K looks mighty attractive, as does the 'spare' memory on a CGA 
card...BUT...because one may easily forget there are programs in that 
space, switching to Herc graphics, or simulating a CGA, or using a CGA 
in graphics mode will really screw up the works, so this technique is 
not recommended.  It may be used to test out the program, though, and 
see if it's worth the small trouble to get memory for the 'safe' areas.


                         HOW THE PROGRAM WORKS

HILOAD grabs the program you want, as well as any command tail required, 
and loads it into the memory area you specify. After loading the 
candidate TSR program, it revectors several DOS interrupts and then 
executes the TSR program in the new location. When the TSR program 
attempts to 'go resident', HILOAD traps that request, either from INT 
27H or function 31H of INT 21H, resets the appropriate interrupt 
vectors, examines the interrupt vector table to see which ones point to 
the new program, and then terminates normally.

Thus, when HILOAD exits, zero DOS memory is used up, and the TSR is 
snugly nestled in another part of memory, acting just like it normally 
does.

                     HOW TO SPECIFY VARIOUS THINGS

HILOAD requires various pieces of information to operate properly.

Addresses  -    HILOAD requires a starting address for 
                placing TSR's. After it places the first 
                one, it keeps track of where it should place 
                the next one by using the Intra-application 
                Communication Area (ICA) at 0040:00F0 
                through 0040:00FF. It checks this area and 
                computes an address from the information 
                there, so the initial starting address has 
                to be specified only once (until you change 
                blocks). As long as the loading area is 
                contiguous, the starting address need not be 
                re-specified.

                The starting address is specified by an en- 
                vironment variable, which is discussed be- 
                low.

Program names - The program name to be loaded must be 
                specified with the full path name.  Sorry 
                about this, but it wasn't worth the effort 
                to program the logic to chase down the paths 
                to find the programs.  This is not consid-
                dered (by me, anyhow) to be a serious ob-
                jection, as the typical use of this program
                is in your AUTOEXEC file where it is only
                typed in once.

Starting off -  Executing HILOAD without any program 
                specified causes it to zero out the ICA.  
                This is the easiest way to begin a loading 
                sequence after changing the start address.


           SPECIFYING A START ADDRESS (ENVIRONMENT VARIABLES)

When DOS loads a program, it also provides that program with a copy of 
what it calls the Environment.  To see what the contents of your 
environment are, do the following:

        At the DOS prompt (e.g., C:\>), type SET <CR>

The response will be a list of things, starting with COMSPEC and 
continuing with your PATH and PROMPT values (if you have any).  After 
these values, you may or may not have additional entries.  If you do, 
they will be of the form:

        name=value

To add a value to the environment, type:

        set abc=ABCabc <CR>

and then type

        set <CR>

Notice that a new environment variable has been added.  Notice also that 
the name, abc, has been capitalized as ABC, but the value remains as it 
was typed in, i.e., ABCabc.

To change an environment value, type

        set name=NewValue<CR>

and NewValue will replace the old value.

To delete an environment variable, type

        set name=<CR>

and the value will disappear from the environment.

HILOAD requires an environment variable with a name the same as the 
program name.  The value is the hex starting address.

So, if the program is named HILOAD, as it is on this disk, and the 
desired starting value is A000, then you would set the environment 
variable by typing:

        set hiload=A000<CR>

This can also be done as an entry in your AUTOEXEC.BAT file.

DOS is poorly documented, but it provides the name of the program it 
loads, and where it came from, right after the environment.  I have used 
this quirk of DOS to determine the name of the environment variable. If 
you change the program name to, say, SHIFTSR.COM, then you would set the 
environment variable as:

        set shiftsr=A000<CR>

This feature (?) allows you to have multiple copies of the program under 
different names, each with its own environment variable, if you should 
so desire.

NOTE:  As far as I can tell, this feature is only available in DOS 3.X.  
The program determines the DOS version in use and, if less than 3.0, it 
uses a default program name of HILOAD.  This is what the name of the 
environment variable would have to be, no matter what you rename the 
program to.


                        INITIALIZING THE PROCESS

As stated above, the program must first initialize the ICA. It does this 
by being invoked with no parameters.  The 'standard' starting sequence 
is therefore:

        SET HILOAD=A000
        HILOAD
        etc.


                      SPECIFYING PROGRAMS TO LOAD

Also as stated above, full path names must be given.  Suppose you have 
four TSR's you wish to load, as follows:


        NAME            SIZE            PARAMETERS (TSR command tail)

        TSR1             14K                 none
        TSR2             22K                 /X /U /M=22
        TSR3             1.4K                none
        TSR4             26K                 'text string'

Adding them up, we see that they will occupy less than 64K, so they can 
all be loaded in one block. Suppose also we have the A block available 
for use.  The series of commands in the AUTOEXEC file to perform the 
desired action might be:


        SET HILOAD=A000                         starting address
        HILOAD                                  initialize
        HILOAD \DOS\TSR1                        load first tsr
        HILOAD \SUB1\SUB2\TSR2 /X /U /M=22      load next tsr
        HILOAD \TSR3                            load next tsr
        HILOAD \UTILITY\TSR4 'text string'      load last tsr

The directories shown are the complete path names
to the various TSR's.

Suppose now you have another TSR you want loaded, but it's too big to 
fit in the A block; you have memory available in D block.

You would follow the above sequence with:

        SET HILOAD=D000                         reset start address
        HILOAD                                  re-initialize
        HILOAD \SUB3\SUB4\TSR5                  load it


                             PROGRAM OUTPUT

HILOAD issues various progress and error messages as it chugs along. It 
tells you the starting address it uses, the name of the program it is 
loading, what it found for a command tail to the TSR, and the amount of 
memory the TSR has reserved for itself.

It also lists the interrupts the TSR has captured, along with their new 
addresses.  This can be handy for debugging purposes or just finding out 
who captures what. Many TSRs do not go through Int 21H functions 35H and 
25H to get and set the interrupt vectors; they directly manipulate the 
DOS interrupt table at the bottom of memory.  This is not a recommended 
technique but many do so. HILOAD will capture these villians (SideKick 
being the most prominent one) and show what they trap.

Incidentally, it appears that SideKick traps interrupt 21H for itself, 
and any TSR loaded after it, who attempts to grab Int 9H, is pushed down 
the list by SideKick so he (SideKick) still has first grab at the 
keyboard. Very clever programming; a pain in the kazoo when you're 
groping around to figure out what's actually happening!

The above comments are based on an older version of SideKick (1.56) 
which I have been using. Later versions may act in a more civilized 
manner.


                           KEEPING THE OUTPUT

Since the information from HILOAD can whiz off the screen before you 
have a chance to read it, it is a good idea to redirect the output to a 
file instead of the screen.  The program output can then be perused at 
your leisure. The following sequence is an example of how to do this:


        DEL TSRLIST.LST                           delete old file
        SET HILOAD=A000                           set start address
        HILOAD >>TSRLST.LST                       initialize
        HILOAD \TSR1 >>TSRLST.LST                 load first tsr
        HILOAD \SUB1\TSR2 /X /Z >>TSRLST.LST      load next tsr
        SET HILOAD=D000                           reset start address
        HILOAD >>TSRLST.LST                       initialize
        HILOAD \UTILITY\BIGTSR /PARMS >>TSRLST.LST  load big tsr

After everything is loaded, the file TSRLST.LST may be browsed to see 
what went on, get addresses, check vectors, etc.

Of course, the output may also be redirected to the printer by putting a 
>PRN instead of >>filename.ext


                             ERROR MESSAGES

If something doesn't go right, the program tries to tell you and exit 
safely.  The error messages are:

        No address given ... ABORTING          Something's wrong with the
                                               environment variable. Check
                                               spelling of variable name and
                                               make sure it agrees with the
                                               program name.
                                               The value given must be 4 hex
                                               digits, upper or lower case.

        Can't find file PROGNAME ... ABORTING   HILOAD was unable to locate
                                                the specified program. Check to
                                                see that the path is correct.
                                                Also, only .COM files can be
                                                loaded this way; .EXE files
                                                will bomb!

        Requires DOS 2.0 ... ABORTING           Program requires DOS version
                                                2.0 or above.

        The program also issues a message when it initializes the ICA.


                               DISCLAIMER

TSRs are tricky things; SideKick is notorious for being sensitive to the 
order in which other TSR's are loaded. Experiment with loading your TSRs 
in the 'normal' fashion until you get a loading sequence that works. Use 
that order to HILOAD them and all should be well.


                              LEGAL STUFF

This program is being placed in the public domain.  It may be copied and 
distributed freely for non-commercial uses.  Both this file and the 
executable code must be distributed together and unmodified.

Any brand names mentioned are copyright by their respective owners.


                           SHEEPISH ADMISSION


This program was developed over a period of time as I was learning about 
TSRs and revectoring interrupts, etc. Also, though the objective of the 
program remained firm, the little niggly details kept changing on me as 
I thought of alternate ways to accomplish things and more frills were 
added.  

Consequently, the source code is comprehensible to me but I'm sure looks 
like a real mess to the 'seasoned professional'.  I am thus a little 
ashamed to release it for public scrutiny and scorn.

However, it is included and commented as best as I can recall what each 
little piece does.  Don't bother to tell me there are 'dead code' areas 
and unused variables.  

Anybody who wants can modify it to their hearts' content, but please 
take note of the distributon restriction noted above.


                          Larry Shannon 
                          5615 Truscott Terrace
                          Lakeview, NY  14085

                                - end -

         ----------------end-of-author's-documentation---------------

                        Software Library Information:

                   This disk copy provided as a service of

                        The Public (Software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  The P(s)L cannot de-
         bug programs over the telephone.

         Disks in the P(s)L are updated monthly, so if you did not get
         this disk  directly from the P(s)L,  you should be aware that
         the files in this set may no  longer be the current versions.

         For a copy of the latest monthly software library newsletter
         and a list of the 2,000+ disks in the library, call or write

                        The Public (Software) Library
                              P.O.Box 35705 - F
                           Houston, TX 77235-5705
                            Orders: 800-2424-PSL
                            Info:   713-524-6394
                            FAX #:  713-524-6398
                            CIS ID: 71355,470